C-540, C-440 and C-340 Element

Furnish and install C-540, C-440 and C-340 fin-tube heating elements as manufactured by Slant/Fin Corporation, consisting of 1 1⁄4" nominal* copper seamless-drawn tubing* with 4 1⁄4" x 4 1⁄4"x .020" aluminum fins spaced 40 per linear foot. Fins shall be mechanically bonded to the tubing to increase thermal contact and to space and lock the fins uniformly in place. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element shall be expanded to receive the expanded end of

another, without couplings.

* C-440 is 1" copper pipe. C-340 is  3⁄4" copper pipe.