E-75E Element

Furnish and install E-75 baseboard heating element as manufactured by Slant/Fin Corporation, consisting of  3⁄4" nominal copper tubing  with  2 5⁄8" x  2 1⁄8"x .009" aluminum fins, bent to 2 5⁄16"x 2 1⁄8", spaced 55 per linear foot. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. End fins are of plated steel for extra ruggedness. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.