H-3 Element

Furnish and install H-3 baseboard heating element as manufactured by Slant/Fin Corporation, consisting of  3⁄4" nominal copper tubing, with  3 5⁄32" x  2 1⁄2" x .011"aluminum fins bent to 2 3⁄4"x 2 1⁄2", spaced 55 per linear foot. Fins shall be mechanically bonded to the tubing to increase thermal contact and to space and lock the fins uniformly in place. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.