S-540, S-532  and S-832 Element

Furnish and install S-540 and S-532 fin-tube heating element as manufactured by Slant/Fin Corporation, consisting of 1 1⁄4" IPS steel pipe* (Schedule 40), with 4 1⁄4" x 4

1⁄4"x .024"steel fins spaced 40 per linear foot for S-540 and 32 per linear foot for S-532 and S-832. The pipe shall be forced through undersized fin holes to obtain a force-fit mechanical bond.  A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. Both ends of each element pipe shall be threaded with IPS standard threads

* S-832 is 2" IPS steel pipe