F & EM Series

Furnish and install as shown on the plans “F” or “EM” Series flat-top enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin Corporation. Cover shall be of one piece construction. Enclosure shall be EM-5, EM-12, EM-19, F-5, F-12 or F-19 and shall have (1,2 or 3) tier element. EM enclosure shall be made of expanded steel. F enclosure shall consist of stamped top grille with pencil-proof air discharge louvers.

Covers shall be fabricated from 18-gauge (16-gauge for EM) steel in electro galvanized finish or as custom color matched as per specification.

Brackets and hangers shall be channeled steel in electro galvanized finish. Fin-tube element(s) shall be Model_________.   Provide lengths and capacities as scheduled on plans.

Furnish required channeled bracket-hanger assemblies for rigid element support.

Provide all required accessories for complete installation. Enclosure accessories in bonded zinc steel shall be telescopic and match enclosure color