FS Series

Furnish and install as shown on the plans “FS” Series free standing enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin Corporation.

Cover shall be of one piece construction. Enclosure shall be (FS-7, FS-14, FS-21) and shall have (1,2 or 3) tier element. Top part of enclosure electro galvanized shall consist of stamped grille with pencil-proof air discharge louvers. All enclosures shall have female to female slip joint connection with interlocking internal splice. The internal splice provides additional strength with a nearly invisible joint.

Cover shall be fabricated from 18 (16 or 14) gauge galvanized steel or as custom color matched as per specification.

Brackets and hangers shall be channeled steel in hot dipped wiped coat galvanized finish. Brackets and hangers shall be Model_____________. Provide lengths and capacities as scheduled on plans.

Furnish required channeled bracket-hanger assemblies with heavy floor mounting flange for rigid front skirt and element support.

Provide all required accessories for a complete installation. Enclosure accessories in electro galvanized steel shall be telescopic and match enclosure color