Select one of the following H elements to specify:

H-1 Element

Furnish and install H-1 baseboard heating element as manufactured by Slant/Fin Corp.

consisting of 3/4" nominal copper tubing, with 3" x 3-1/4" x .024" aluminum fins, spaced 48 per linear foot. The tubing shall not be weakened by expansion in process of manufacture, but shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.

H-3 Element

Furnish and install H-3 baseboard heating element as manufactured by Slant/Fin Corp.,   consisting of 3/4" nominal copper tubing, with 3-5/32" x 2-1/2" x .011" aluminum fins bent to 2-3/4" x 2-1/2" spaced 55 per linear foot. The tubing shall not be weakened by expansion in process of manufacture, but shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.

H-4 Element

Furnish and install H-4 baseboard heating element as manufactured by Slant/Fin Corp.,   consisting of 1" nominal copper tubing, with    3-15/32" x 2-1/2" x .011" aluminum fins bent to 3" x 2-1/2" spaced 48 per linear foot. The tubing shall not be weakened by expansion in process of manufacture, but shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.

H-5X Element

Furnish and install H-5 baseboard heating element as manufactured by Slant/Fin Corp.,   consisting of 1-1/4" nominal copper tubing, with 3" x 3-1/4" x .020" aluminum fins spaced 48 per linear foot. The tubing shall not be weakened by expansion in process of manufacture, but shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element tube shall be expanded to receive the unexpanded end of another, without couplings.

H-6X Element

Furnish and install H-6 baseboard heating element as manufactured by Slant/Fin Corp.,   consisting of 1-1/4" IPS steel pipe (Schedule 40), with 3" x 3-1/4" x 0.028" steel fins, spaced 48 per linear foot. The pipe shall not be weakened by expansion in process of manufacture, but shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. Both ends of each element pipe shall be expanded to be threaded with IPS standard threads.