HD Series

Furnish and install as shown on the plans model __________ HD Series slope-top baseboard with element, required mounting components and accessories as manufactured by Slant/Fin Corporation. Complete two-piece enclosure assembly shall consist of full back panel with interlocking slope top front panel, factory packaged with necessary brackets.

Front cover shall be fabricated from 16-gauge galvanized steel, back panel from 20-gauge galvanized steel. The front panel & accessories shall be finished in galvanized finish or as custom color matched as per specifications.  Fin-tube element(s) shall be Model___________. Provide lengths, heights and capacities as scheduled on plans.

Bracket with element hanger shall be spot welded to back panel every 12 inches. There shall be dimpled anchoring holes every 12 inches on front cover. Use 8 x 3/8" self-tapping screws with countersunk heads to fasten front cover to brackets. Screws recess into dimpled anchoring holes on front cover. Screws are supplied in carton with cover.

Provide all required accessories for a complete installation. Cover accessories shall be telescopic to eliminate the need to perfectly butt one length of cover to the next. Accessories to be fastened with screws (pan-head) supplied by others.