J Series, JA-14, JA-21 or JA-28 Series

Furnish and install as shown on the plans JA slope-top fin-tube enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin Corporation. Cover shall be of onepiece construction. (A knob-actuated damper shall be provided.) Top part of enclosure shall consist of stamped grille with pencil-proof air discharge louvers. (Optional: A knob-actuated damper shall be provided.)

Cover shall be fabricated from 18 (16 or 14) gauge galvanized steel. Cover finish shall be galvanized or powder coated to a color as per specification. Brackets and hangers shall have a galvanized finish. Cover panels to join using Internal Splice Plates, resultant joint has covers butting to one another resulting in a clean joint without unsightly weld marks on front of cover.

(Optional: Cover with anodized aluminum grill in place of pencil-proof louvers. Cover shall be fabricated from 18 (16 or 14) gauge galvanized steel. Cover finish shall be galvanized or powder coated to a color as per specification. Brackets and hangers shall have a galvanized finish. Covers panels shall join using slip joint resulting in a clean joint.)  Please note that knob-actuated damper is not available on aluminum grill cover.

(Optional: A full height back panel shall be provided of 20 gauge galvanized steel.)

Provide all required accessories for complete installation. Cover accessories shall be telescopic and shall match enclosure color. Fin-tube element(s) shall be Model___________. Provide lengths and capacities as scheduled on plans. Furnish required channeled bracket-hanger assemblies with heavy flag brace for rigid front panel and element support.