LC Series

Furnish and install as shown on the plans model (LC-850, LC-1400) LC Series-slope top baseboard with element, required brackets and accessories as manufactured by Slant/Fin Corporation.

Front Cover shall be fabricated from 18-gauge galvanized steel. Top horizontal lip of cover shall be no wider than 7/8 inch, this is to prevent standing on the cover.  Outlet louvers shall be located on the front sloped face of the cover, louvers located on the top of the cover are not acceptable.  Cover finish shall be galvanized finish

or custom color matched as per specification.

Front cover to be mounted on the wall with one piece wall brackets. Brackets shall be spaced no further than 2 feet apart with bracket secured to wall studs and not to the wall board. Slide-action expansion cradles shall be inserted between heating element and cover brackets. Slide-action expansion cradles are supplied with heating element.  Installer shall secure front cover to mounting brackets by drilling hole into vertical flange on lower front cover and screwing front cover to each wall bracket. Screws are field supplied.

Finned tube heating element shall be Model ______.  (One, Two) tiers of element to be installed within cover.  Provide lengths, heights and capacities as scheduled on plans. (Add specification for model of element being specified).

Provide all required accessories for a complete installation. Accessories shall be telescopic to eliminate the need to perfectly butt one length of cover to the next.  Accessories to be fastened with pan head screws to front cover, screws are field supplied.