Cover Assembly

Furnish and install as shown on the plans Multi/Pak®90—slope-top fin-tube enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin. Cover shall be of two interlocking sections: a top cover and front cover.  Top cover will be common to one-tier (90-14) and two tier (90-21) models. (Optional: A knob-actuated damper shall be provided). Top cover shall consist of stamped grille with pencil-proof air discharge louvers. Front cover shall interlock with top cover to form lateral decorative panel. Front cover shall be removable without removal of the top cover.  Interlocking top cover and front cover shall both be fabricated from 18-gauge galvanized steel in pre-painted Nu-White baked enamel finish or color as per specification. Brackets and hangers shall have a galvanized finish.

Provide and install Slant/Fin's internal splice plate. The internal splice plate shall provide an internal slip connection without creating unsightly weld marks on the front of the cover. The resultant joint will be a neat butt joint; the need for an external splice plate is eliminated.

Fin-tube element(s) shall be Model___________. Provide lengths and capacities as scheduled on plans. Furnish required channeled bracket-hanger assemblies with heavy flag brace for rigid front panel and element support. Provide all required accessories for complete installation. Cover accessories shall be telescopic and shall match enclosure color.