Select one of the following S or C elements to specify:

C-540, C-440 and C-340 Element

Furnish and install C-540, C-440 and C-340 fin-tube heating elements as manufactured by Slant/Fin, consisting of 1¼” nominal* copper seamless-drawn tubing* with 4 ¼” x 4 ¼” x .020" aluminum fins spaced 40 per linear foot. Fins shall be mechanically bonded to the tubing to increase thermal contact and to space and lock the fins uniformly in place. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. One end of each element shall be expanded to receive the expanded end of another, without couplings.

*C-440 is 1" copper pipe. C-340 is 3/4" copper pipe.

S-540, S-532 and S-832 Element

Furnish and install S-540 and S-532 fin-tube heating element as manufactured by Slant/Fin, consisting of 11/" IPS steel pipe* (Schedule 40), with 41/" x 41/"x .024"steel fins spaced 40 per linear foot for S-540 and 32 per linear foot for S-532 and S-832. The pipe shall be forced through undersized fin holes to obtain a force-fit mechanical bond. A flange with four teeth shall be formed on each fin to increase thermal contact and to space and lock the fins uniformly in place. Both ends of each element pipe shall be threaded with IPS standard threads.

*S-832 is 2" IPS steel pipe.