TBG Series

Furnish and install as shown on the plans “TBG” Series top & bottom slope enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin Corporation. Cover shall be of one piece construction. Enclosure shall be (TBG-17, TBG-24) and shall have (1 or 2) tier element. (A knob actuated damper shall be provided.) Top and bottom slope of enclosure shall consist of stamped grille with pencil-proof air discharge louvers. All enclosures shall have female-to-female slip joint connection with interlocking internal splice. The internal splice provides additional strength with a nearly invisible joint. (Optional: A full height back panel shall be provided of 20-gauge steel in hot dipped wiped coat galvanized finish.)

Cover shall be fabricated from 16 gauge (14 gauge option) steel in galvanized finish or as custom matched as per specification.

Brackets and hangers shall be channeled steel in hot dipped wiped coat galvanized finish. Fin-tube element(s) shall be Model_________. Provide lengths and capacities as scheduled on plans.

Furnish required channeled bracket-hanger assemblies with heavy channeled bracket for rigid front skirtand element support.

Provide all required accessories for a complete installation. Enclosure accessories in electro-galvanized steel shall be telescopic and match enclosure color.