GXHT Series Caravan Hot Steam Gas-Fired Specification

Furnish and install, in compliance with manufacturer’s instructions and the rules and regulations of the authorities having jurisdiction.

Modular boilers shall have a C.S.A. input of ________BTUH natural (LP) gas with a gross output of ________ BTUH, Net A.H.R.I. rating of _______ BTUH and E.D.R. (Sq. Ft.) Steam rating of ______. Boiler shall be Slant/Fin Caravan Model _______ consisting of ____ modules or approved equal.

Heat exchanger shall be fabricated from cast iron vertical sections. Water seal between sections shall be metal push nipples, gasket material is not acceptable. Each module shall be constructed in accordance with Section IV of the ASME boiler and pressure code for low-pressure steam boilers with a maximum working pressure of 15 PSIG. Each module shall be equipped with a pressure gauge.  The ASME steam relief valve capacity shall exceed each modules gross output, the installer shall pipe each relief valve to within 6 inches of the floor to a location that will show visible signs of discharge. All cast iron sections shall have a ten-year manufacturer’s warranty.

Modules shall have a thermal efficiency of____ %. Each module shall have a corrosion resistant, aluminized steel base assembly lined with ceramic fiber refractory type combustion chamber. Each module shall be equipped with stainless steel port ribbon burners with reverse slot design to prevent flame flashback. Each module shall be equipped with intermittent pilot ignition (IID) system, combination redundant gas valve with manual shut off, pressure regulator, pilot adjustment and 100% shut off. Each module shall be installed with factory supplied draft hood.

Each module shall be equipped with a PA404A pressure control, electronic low water cut-off, water sight glass, pressure gauge, ASME 15 PSI steam pressure relief valve, drain valve, flame rollout switch and draft hood with blocked vent switch to interrupt power to the gas valve in the event of a related unsafe condition.

Modules shall be factory assembled and tested. A heavy gauge steel, insulated factory installed jacket shall enclose the cast iron heat exchanger and gas controls. Each module shall have its own jacket to allow for unevenness in the boiler pad. One jacket for multiple modules is not acceptable.

Installer shall provide, install and test manual reset high pressure control and manual reset low water cut-off.

The heating plant floor load shall not exceed 125-pounds/square foot filled with water. For maintenance, the module design shall permit complete access to controls, burner, relief valve, temperature/pressure gauge and drain valve from the front of the modules.

Optional equipment:

(Vent Damper)

(List factory representative start-up supervision)